## Slide 1: FLImBRUSH data processing

## Slide 2: truncation window for PpIX
 | ENOB=7(manual) | ENOB=8 | From measurement data
Noise | 0.0156 | 0.0078 | 0.035
I just took the middle road

## Slide 3: FLImBRUSH acquisition window
Current FLImBRUSH acquisition:
Total: 500 points*0.4 ns/points = 200 ns.
Data after peak: 106 ns (17ns short for slowest iRF).
Solution: We can adjust the trigger delay by 50ns.

## Slide 4: Alpha vs Condition value
Sampling rate (GS/s) | Truncation length | Eps = 1.01 | Eps = 1.0001
20 | 3080 | 0.9837 | 0.9808
10 | 1540 | 0.9677 | 0.9619
5 | 770 | 0.9365 | 0.9252
2.5 | 385 | 0.877 | 0.856
We have been using 1.0001 for the past

## Slide 5: Simulation
Lifetime range: 0.3-20ns
Gaussian white noise: 55dB SNR (good approximatin for FLImBRUSH)
Truncation window = 154ns (PpIX)

## Slide 6: 20 GS/s

## Slide 7: 10 GS/s

## Slide 8: 5 GS/s

## Slide 9: Observation
Adding noise increase the std of lifetime (how surprise :p)
The effect of condition value (1.01 vs 1.0001) is minimum. The biggest different is for lifetime > 16ns.
Small bias(~0.1ns) as a function of lifetime(shorter lifetime, longer lifetime)

## Slide 10: Result from dye measurements
2 decon setting:
  154ns window(PpIX) with its corresponding alpha
  54.4ns window(matching V4) with its corresponding alpha

## Slide 11: V4: 12.5 GS/s, 54.4ns(680 points),alpha = 0.916

## Slide 12: FLImBRUSH: 5 GS/s 154 ns alpha = 0.9252

## Slide 13: FLImBRUSH: 5 GS/s 154 ns alpha = 0.8024

## Slide 14: FLImBRUSH: 5 GS/s 54.4 ns alpha = 0.8024

## Slide 15: 5 GS/s, 54.4 vs 154 ns, alpha = 0.8024
154ns lifetime – 54.4ns lifetime

## Slide 16: FLImBRUSH: 10 GS/s 154 ns alpha = 0.9619

## Slide 17: FLImBRUSH: 10 GS/s 154 ns alpha = 0.8958

## Slide 18: FLImBRUSH: 10 GS/s 54.4 ns alpha = 0.8958

## Slide 19: 10 GS/s, 54.4 vs 154 ns, alpha = 0.8958
154ns lifetime – 54.4ns lifetime

## Slide 20: FLImBRUSH: 20 GS/s 154 ns alpha = 0.9808

## Slide 21: FLImBRUSH: 20 GS/s 154 ns alpha = 0.9465

## Slide 22: FLImBRUSH: 20 GS/s 54.4 ns alpha = 0.9465

## Slide 23: 20 GS/s, 54.4 vs 154 ns, alpha = 0. 9465
154ns lifetime – 54.4ns lifetime

## Slide 24: 10 GS/s 154 ns alpha = 0.9619
Effect of noise in the tail
So it is not the averaging

## Slide 25: Decays: 10 GS/s 154ns different alpha
The decay always deviate around 250 point(25ns) for all channels, related to when decay drop below noise?
The data have different length because the tail of the data sometime go to very small negative value less than ~-10e-7, which can not be displayed in log scale
I didn’t notice any pattern for the when negative value happens, but it also present in V4 data as well. I think it might be related to the tolerance of the algorithm.

## Slide 26
If we use a representative irf based on data and compute the truncation length? (irf for all 3 channel are similar)
~ 25ns, the data drop below noise

## Slide 27
What if we truncate the decays to 250 points (25ns) and compute lifetime?
The lifetime is with in 0.1ns
So the noise in the tail cause the decay to drag long.

## Slide 28: DC

## Slide 29: Summary
Using 154ns window for 4ns decay cause more harm than good
  The lifetime value is consistently longer for all sampling rate.
  The std of deconvolved data is larger. Consistent across sampling rate. This mean the alignment of waveform is no longer the limiting factor for std.
Should use a truncation window that match the expected lifetime
Hard to tell why 1/e lifetime seems better for long window